# Service Bulletin

No. 91-008

Optional	TIMELINE VISTA, INC.

1755 LA COSTA MEADOWS DRIVE

RECOMMENDED	SAN MARCOS, CA  92069

Tel. 760-761-4440

Mandatory	(FAX 760-761-4449)

SUPPORT@DIGAUDIO.COM

## Bi-phase Lockup Time Improvement

### DATE:	01/29/93

### MODEL:	Lynx Film Module

### REVISION:	All

### SERIAL NO:	4000 and below

### SOFTWARE:	All

### REQUIRED TOOLS:

Static safe workstation	Phillips screwdriver
Grounding wrist strap	Soldering iron and solder remover

### REQUIRED PARTS

TimeLine Part Number 21C010; Capacitor, Poly .220 f, 50 V

### DESCRIPTION:

Change C9 on the Film Processor Printed Circuit Board to 0.22 f from 1.0 f, to improve lock up time by one second.

### PROCEDURE:

1.	To access the Lynx Film Board, turn off the power and disconnect all cables from the Lynx module.

2.	On a static safe workstation, remove the six phillips screws securing the chassis top cover.  Remove the chassis top cover.  See Figure 1.

3.	Remove the four screws holding the film processor board (top board) in place.

4.	Disconnect ribbon cables P4 and P5 and lift the film board out of the Lynx Module.  Place the board on a static safe workstation.

Figure 1.  Remove the Film Processor Board

### PROCEDURE (continued):

5.	Locate C9, the 1.0 f capacitor and remove it.  See Figure 2.

6.	Install a .22 f capacitor into position C9.

Figure 2.  Location of C9

7.	Place the film board back on the standoffs in the Lynx Module.

8.	Insert and tighten the phillips screws into the standoffs.  Reconnect ribbon cables P4 and P5.

9.	Replace the cover, insert and tighten the six phillips screws.