Gearbox Installation Guide

Lynx Film Module

TIMELINE VISTA, INC.

1755 LA COSTA MEADOWS DRIVE, SUITE B

SAN MARCOS, CA  92069

TEL. 760-761-4440

(FAX 760-761-4449)

SUPPORT@DIGAUDIO.COM)

DATE:	8/4/92

MODEL:	Lynx Film Module

REVISION:	All

SERIAL NO:	All

SOFTWARE:	N/A

REQUIRED TOOLS:

Static safe workstation	IC Extractor/Insertor or 
	Grounding wrist strap	small slotted screwdriver
	Phillips screwdriver		Wire side cutters

REQUIRED PARTS:

71B014 Film Gearbox Processor Kit

PROCEDURE:

1.	Turn off the power to the Lynx Film Module. Disconnect all cables.

- Place the Lynx on a static safe workstation. Ground yourself and the workstation 
anti-static mat.

- Remove the 6 phillips screws holding the top cover to the chassis. Remove the top cover.

Figure 1.  Remove the Top Cover

4.	Disconnect ribbon cables P4 and P5 from the film processor board (top board).

5.	Remove the five screws holding the film processor board and put the board on a static safe workstation.

6.	With the Lynx front panel facing you, locate and remove the PROM(s), U16 , U7 (if fitted), and U48 the micro processor. See Figure 2.

PROCEDURE continued:

WARNING
Use an IC insertor to remove U7, U16 and U48. If one is not available, use a small slotted screwdriver. 
Insert the screwdriver under the IC’s, twist slightly and gently lift up. Inserting the screwdriver incorrectly 
could damage surrounding components.

7.	Locate and install the new PROM into U16. Be careful to correctly align Pin 1 and properly seat the PROM. Check that Jumpers JP1 and JP4 are in the 512K position as indicated in  Figure 2.

Figure  2.  PROM and Jumper Configuration

8.	Hold the gearbox processor card so that the 40 pin header can easily be plugged into U48, 
the processor socket.  Be careful to correctly align all the pins and then press the header down firmly. See Figure 3.

Figure 3.  Installation of the Gearbox Processor Board

PROCEDURE continued:

9.	To ensure clearance for the gearbox board the film processor board component leads, directly above the gearbox processor must be closely trimmed.  On the solder side, trim the leads on U18 and surrounding components, indicated in Figure 4, with wire side cutters.

Figure 4.  Film Processor Modifications

10.	Insert the five standoff mounting screws into the film processor board.

11.	Push the supplied fiber washers onto each screw.   Place the film processor board on the standoffs and tighten the five phillips screws. Reconnect ribbon cables P4 and P5.

12.	Check all connections and replace the top and bottom covers on the Lynx Film Module. Insert and tighten the phillips screws. Reconnect the cables and turn on the power. 
The Lynx Film Module will automatically detect the gearbox processor. To verify that the upgrade is operating, the new software version number will be displayed after turning the power on.