No. 95-004

Optional	TIMELINE VISTA, INC.

1755 LA COSTA MEADOWS DRIVE, SUITE B

Recommended	SAN MARCOS, CA   92069

Tel. 760-761-4440

Mandatory	(FAX 760-761-4449)

SUPPORT@DIGAUDIO.COM

## Lynx Studer A800 Cable Modification

### DATE:	08/31/95

### MODEL:	Studer A800 Cable (TimeLine Part Number 71C025)

### REVISION:	All

### SERIAL NO:	Serial Numbers under 5078

### SOFTWARE:	N/A

### REQUIRED TOOLS:

Soldering iron

### REQUIRED PARTS:

(2) Hirose Male Pins, TimeLine Part Number 34W002

### DESCRIPTION:

This modification is adding Mute Relay N/O to the Studer A800 cable.

### PROCEDURE:

1.	At the Lynx end of the cable (Connector A), add a pin to the Green (Red) pair.  Install into Pin 46 of Connector A, as shown in schematic 70D038.

2.	At the Lynx end of the cable (Connector A), add a ground wire and pin to the Black (BRN) pair.  Install into Pin 48 of Connector A, as shown in schematic 70D038.