# Installation Guide

For Studer "B" Cables

TimeLine Vista, Inc.

1755 LA COSTA MEADOWS DRIVE, SUITE B

SAN MARCOS, CA  92069

TEL. 760-761-4440

(FAX 760-761-4449)

SUPPORT@DIGAUDIO.COM

### DATE:	02/05/93

### MODEL:	Lynx Time Code Module
	Lynx-2 Time Code Module

### REVISION:	All

### SERIAL NO:	All

### SOFTWARE:	All

### REQUIRED PARTS:

Lynx Time Code Module
    Studer "B" Cable, with "serial card interface", TimeLine P/N 71C033

Lynx-2 Time Code Module
    Studer "B" Cable, TimeLine P/N 71C034

Studer Machine
    Serial Interface, Studer P/N 1.810.752.00
    (Not required for A-807, which has serial interface built-in)

### DESCRIPTION:

TimeLine Studer Serial Interface will allow:

Serial machine control

Individual track select from KCU

Improved locates and searches

### PROCEDURE:

On all but the A-807, the studer serial interface is an optional part from Studer.  It is built-in on the A-807.  Studer Serial Interface, part number 1.810.752.00, is required for all other machines.

### Software requirements for individual Studer machines are:

A-807 = 10/89 or later (Serial control only available on machines with serial numbers higher than 08807)

A-810 = 6/89 or later

A-812 = 4/90 or later

A-820 (2 track) = 6/89 or later

A-820 (multi) = 2/90 or later

A-827 = 5/91 or later

### PROCEDURE Continued

### Studer serial port mode/settingsfor A-820 and A-827:

9600 baud

No parity

One stop bit

No echo

### Other Studer settings:

A-820/A-827:  Auto input should be switched off on TC track to improve search and park accuracy, as well as lock-up time.

A-820 (2 track):  Switch DELAY OFF for fastest lock-up time.

Warning

Rehearse functions on A-820/A-827:
1.  Check menu 44.  Must be set to DELAY ON, otherwise machine will go into RECORD
when rehearse is issued.
2.  If the delay inhibit switch on the Studer machine remote unit is on, the machine will go into RECORD
when rehearse is issued.

### Cables

Older TimeLine Lynx cables may not have the rehearse line connected.

Figure 1.  Rehearse Pin Connector