Manual Supplement

No. MS 94-002

TimeLine Vista, Inc.

1755 LA COSTA MEADOWS DRIVE, SUITE B

SAN MARCOS, CA  92069

TEL. 760-727-3300

(FAX. 760-727-3620)

SUPPORT@DIGAUDIO.COM

## System Supervisor Unit Software Release Notes

### DATE:	4/17/18

### MODEL:	System Supervisor Unit (SSU)

### REVISION:	All

### SERIAL NO:	All

### SOFTWARE:	PROM Name	Version
	MAIN	1.42
	TGEN	1.43
	TRIB	1.42

### MANUAL:	73A006

### DESCRIPTION:

#### TGEN 1.43

The following improvements have been made in the TGEN 1.43 software release:

(	Master/reference time code generator (TCG) is now operational in Rewind, when the time code type is Drop Frame.

### Software History

#### SSU 1.42 Series

The following improvements have been made in the SSU 1.42 software release:

(	SSU Trip Port 3 now supports the Harrison MPC1 Console Automation System.  The Supervisor generates serial information that contains master transport status and reference time code for the console.

(	Internal support for the TimeLine Remote Motion Control Unit (RMC) when connected to the SSU Logic I/O Port has been improved.

(	GPI duration calculation and battery backup for GPI registers now work correctly.

(	Neve Flying Faders Automation software versions (1.2/2.X/3.X) are now automatically detected so that differences in Auto-record operation are handled correctly.

### DESCRIPTION (continued):

#### SSU 1.42 Series (continued)

(	SSL Stripe Mode is now fully functional with the latest SSL G Series and Ultimation Automation software.

(	The Supervisor correctly handles record entry from stop.