# Dealer Information Guide

Console Control Unit

TimeLine Vista, Inc.

1755 LA COSTA MEADOWS DRIVE, SUITE B

SAN MARCOS, CA  92069

TEL. 760-761-4440

(FAX 760-761-4449)

SUPPORT@DIGAUDIO.COM

### DATE:	06/17/97

### MODEL:	Console Control Unit

### REVISION:	All

### SERIAL NO:	All

### SOFTWARE:	All

### DESCRIPTION:

Neve V Series Consoles

On Neve Consoles, the area at the top of the Flying Faders Keyboard (above the Smart Keys 1-10) is either a spare blank panel, or a Return Talk Back Speaker and Controls.  When this space is used for a CCU, a new top panel is required.

NOTE:  This new top panel is supplied by Neve in all Flying Faders Automation RETROFITS to Neve V Series consoles.

It may also be necessary to replace the inner subpanel as well.

If there is a return talkback speaker fitted, order a new inner panel.

If there is no speaker fitted, remove the gray top panel, and compare the black inner panel to Figure 1.  The CCU will fit, if the panel matches.  If the panel has a rectangular hole without the six round holes above the Smart Keys, a new inner panel must be ordered.

Neve top and inner subpanel details for the CCU are as follows:

TimeLine Part Number 60E004:  Metal Panel Inner Neve Console, Black	$150.00
TimeLine Part Number 60E003:  Metal Panel Top Neve Console, Gray	$300.00

To ensure a troublefree installation, please make sure that all of this information is obtained from the customer before placing an order.

Other Consoles

TimeLine does not provide special metal work for other manufacturers consoles.  Cutout and mounting details to permit mounting the CCU are provided in the CCU template drawing (70A038-13).  Templates and mounting drawings are also available for the RMC and Jog Shuttle units.

Figure 1.  Subpanels