# PROM Installation Guide

## Lynx System Supervisor

q	Optional	TIMELINE VISTA, INC.

1755 LA COSTA MEADOWS DRIVE, SUITE B

q	Recommended	SAN MARCOS, CA   92069

TEL. 760-761-4440

Mandatory 	(FAX 760-761-4449)

SUPPORT@DIGAUDIO.COM

### DATE:	!//#

### MODEL:	Lynx System Supervisor Unit (SSU)

REVISION:	All

SERIAL NO:	All

### SOFTWARE:	Main PROM			U61
	Timing Generator PROM	U21
	Tributary Port PROM	U45

REQUIRED TOOLS:

Static safe workstation	IC Extractor/Insertor or 
Grounding wrist strap	small slotted screwdriver
Phillips screwdriver

REQUIRED PARTS:

Software Information Sheet
Replacement PROMs from TimeLine

DESCRIPTION:

There are three PROMs in the SSU. A software upgrade may require replacement of one or all of the PROMs. Replace all of the PROMs that were shipped to you.

PROCEDURE:

1.	Turn off the power to the SSU. Disconnect all cables.

2.	Place the SSU on a static safe work-station. Ground yourself and the workstation anti-static mat.

3.	Remove the 8 phillips screws holding the top cover to the chassis. Remove the top cover.

4.	Locate the SSU PROMs, U21, U45 and U61. Verify the version numbers and replace the appropriate PROMs with those included in the Upgrade kit.

Insert the new PROMs. Be careful to correctly align pin one and properly seat each PROM.

Figure 1. Remove the Top Cover

## PROM Installation Guide

PROCEDURE continued:

WARNING

Use an IC inserter to remove U21, U45 and U61. If one is not available, use a small slotted screwdriver. 
Insert the screwdriver under the PROMs, twist slightly and gently lift up. Inserting the screwdriver incorrectly could damage surrounding components.

Figure  2.  PROM and Jumper Location

5.	Note the PROM size marked on the label and then check Jumpers JP3, JP6 and JP9. 
If necessary, move jumper location to the correct position.

6.	Replace the top cover. Insert and tighten the 8 screws. Reconnect the cables and turn on the power. The SSU will automatically detect the new software version.